## RTS INSTALL GUIDE

##### August, 2014

### STOP!

### KEEP FROM FREEZING!

### Engines are tested with water only in the cooling system.

### Storage in freezing temperatures will cause damage!

### CHANGE OIL / FILTER

### Engines are tested with original filter and generic oil. It is recommended to change oil / filter after engine is installed and initial test run and heat cycle has been completed.

### INITIAL STARTUP

### It is not unusual for engines to make a reasonable amount of valve train noise / “ticking” when started for the first time. This is normal and will generally go away within 30 seconds or so.  It is natural for oil to drain down over weeks / months of storage.  If you “crank” engine without ignition power for 30-60 seconds will minimize this situation.

### PLEASE READ ALL!

Read the COMPLETE “Install Guide” as it will answer all of your questions!  Some wire hook ups are 12V- Ground and important for proper operation.  Improper hookup WILL result in damage to ECM.

### TH35O, 700R4, TH400, or Powerglide Transmisions – BOLT UP

First off, there are NO issues with physically bolting any of the GENIII engines to these transmissions.  One less bell-housing bolt is used as the newer GENIII blocks are missing the “1 o’clock” hole.  The issues are solely with the torque converter bolt pattern, and snout depth.  Depending on what vehicle your engine came from, you may or may not need an adapter or flexplate modification.

5.3L & 6.0L LQ9 ENGINES:  Most, if not all 5.3’s & 6.0 LQ9’s will need a spacer a longer bolts to be added behind the flexplate as they came with a “dished” flexplate for the 4L60e / 4L65e transmissions.  All GENIII flexplates use the old TH400 converter larger bolt pattern diameter.  So, if you are going to use a TH350 or 700R4 with the standard torque converter you will need to elongate the flexplate converter holes inward, making a smaller diameter pattern.  Or, you can run a TH400 converter on your TH350 or 700R4 and it will bolt right up.  Elongating the holes is usually the most cost effective.

6.0L LQ4 ENGINES: Most, if not all 6.0 LQ4’s came in 2500 series cars and trucks, which had the 4L80E transmission.  A spacer & longer bolts are NOT needed, but the torque convert bolt pattern is still an issue as with the 5.3L when using the smaller TH350 & 700R4 Converters.  If you are using a TH400 Converter, then it will bolt right up and NO adapter or modification is necessary.

### 700R4 Specific: First off, it is not feasible to use a 700R4 with a DBW engine as there is no throttle body mechanism to hook the TV (throttle valve) Cable to.  There are some Internet threads about hooking it directly to the DBW gas pedal, but I don’t recommend it.  For a DBC engine the 700R4 is a little unusual because it has this TV (throttle valve) cable that needs to be hooked to the throttle body with VERY specific geometry to work properly.  The TV cable is NOT a “kick down” cable.  It controls transmission valve body pressure relative to throttle position (load).  A bracket that supports the end of the TV cable will need to be fabricated and attached to the intake manifold near the existing gas-pedal cable bracket.  A universal TV cable from Summit Racing: ATI-702050 works well.  Follow the diagram below for correct throttle body modification.  A cable mounting point needs to be attached or welded to the bottom side of the throttle body 1.10” from the throttle body pivot point.  At full throttle the TV cable should be completely pulled tight. If you are uncomfortable with this procedure have a qualified transmission shop adjust it.  If not properly adjusted serious transmission damage WILL occur, and quickly.

FLEXPLATE MODIFICATION: Using a mill to elongate the holes is best, but a Dremel tool and 1 bit per hole will usually get the job done too.  Check torque converter bolt alignment and snout fitment into flexplate before installing in vehicle.  Shop around for these parts, you can save yourself some money!

Spacer – GM Part# 12563532 ($49.95)

Bolts – GM Part# 19257940 (6 needed, $5.95/each)

# 4L80E TRANSMISSION: If you want to use a 4L80E transmission with full ECM control it is most cost effective to start with a 6.0L LQ4 2500 Truck motor as it came factory with this transmission and it is no problem.  FYI - 4L60E & 4L80E transmissions are NOT directly interchangeable.  The wiring pinout of the trans plug is different, and 2 VSS’s are used versus 1 on the 4L60E.  Besides the wiring difference, the ECM also requires a segment swap as that portion of the transmission control is completely different.  It can be done, but I do not do this conversion.  If you require a 4L80E transmission with any engine other than the 6.0L LQ4 here are a few options:

Manual Shift kit / Vacuum Pressure Modulator 4L80E-3 & 48-MOD: http://www.transgo.com/

This option is the cheapest but you loose all “auto” features and reverses shift pattern.

OptiShift: http://www.optishift.com/index.shtml

PCS: http://www.powertraincontrolsolutions.com/transcontrol.php

### Automatic Shifters

There is a large selection of shifters and styles available.  For offroad use I prefer a “gated” shifter with a modified gate.  With a modified gate, I see no need for a manual transmission valve body, as full automatic mode is nice for basic trails & cruising.  The modified gate will allow you to instantly find reverse with no confusion, but still allow full automatic mode when in “drive”.  These are 2 of the most economical gated shifters that work great for rock crawling and general offroad use, both around $150.00:

B & M Sport Shifter, $154.95 ------ BMM-80776

### TCI Thunder Shifter, $149.50 ------TCI-616131

### Manual Transmissions

### SM420, SM465, NV4500

Several companies sell kits for this, but this is the cheapest way to go.  I have not personally combined and tested these parts.  But from several hours researching this seems to be the cheapest and readily available parts for around $500.00

Flywheel – Ram-1550 from Summit Racing, $275

Pilot Bearing – GM Part# 12557583 from Summit Racing, $22

Pressure Plate & Clutch Disk – Luk 04-049 from Ebay, Amazon, Autozone, $150

Note:	The kit above comes with a pilot bearing but it can’t be used.

You must use the special GM one for the conversion.

Flywheel Bolts – GM Part# 19257940 from Summit Racing, $36

### Fuel Pump & Fuel Pressure – IMPORTANT!

RETURN SYSTEMS (1999-2003):  GENIII engines require about 58psi of fuel pressure. The inlet is 3/8” with a built in regulator.  Supply the 3/8” port with 58+ psi of fuel and use the smaller 5/16” to return unused fuel to the tank.  Note: the OEM fuel-rail mounted regulator is “vacuum referenced” and MUST remain as it is “tuned” for it.  It will register approximately 52 psi at idle, and 58 psi when vacuum increases.

I recommend a serviceable filter pre pump, and a 10 micron filter post pump.  Summit Racing has all these parts.

Fuel Pump, 				$84.95 ------- TFS-25004P

Pre Filter, 				$12.95 ------- RUS-645120

Return System Post Pump Filter		$16.95 ------- SUM-G1512

Adapter – for Filter / Regulator inlet	$11.95 ------- RUS-640940

RETURNLESS SYSTEMS (2004+):  The newer GENIII engines do not have the regulator & return port on the fuel rail.  You can use a special filter / regulator that has a return port built in.  It can be mounted in the rear of the vehicle right after the fuel pump.  The excess fuel is quickly returned to the tank eliminating the need of a return line ran all the way to the engine compartment.  Remember, fuel flow is what keeps fuel pumps cool.  IMPORTANT: If you do not use this type of filter / regulator you MUST verify that you have 58 psi at the fuel rail.  BD Turnkey Engines are tuned with this filter / regulator.  Engine performance & reliability will be compromised if the correct fuel pressure is not maintained!

Fuel Pump, 				$84.95 ------- TFS-25004P

Pre Filter, 				$12.95 ------- RUS-645120

Returnless System Filter / Regulator	$39.95 ------- WIX-33737

Adapter – for Filter / Regulator		$11.95 ------- RUS-640940

Fuel Rail Inlet Adapter 3/8		$10.96 ------- RUS-644003

Fuel Rail Return Adapter 5/16		$17.95 ------- RUS-640863

# A/C Compressor

The A/C compressor is included in the engine turnkey package.  It comes with the factory port blocks but has a/c hoses cut.  The port blocks are easily drilled and tapped to standard NPT threads for “onboard air” applications.  The upper port is the inlet and should be filtered – This is where to add an ounce of synthetic gear oil once in awhile.  The lower port is the pressure side.  I don’t see the need to filter the oil back out, but an inline “unloader / check valve” should be used.

Alternator

There really is nothing to do with the alternator if running it in the factory location.  It is located on the drivers-side, front & top of the motor (see photo on front page). It is tied into the battery via the battery connection and will start charging when the engine is running.  It is often the most difficult to deal with if packaging is tight.  Relocation is sometimes necessary.  My recommendation is to run it in its factory location unless APSOLUTELY necessary.  Relocating it will cost a lot of money.

### Power Steering Pump

The OEM Saginaw pump comes with the turnkey engine package.  Many aftermarket pumps use the same bolt pattern and will bolt into the existing factory bracket.  A new pulley and serpentine belt is often needed.  Unless APSOLUTELY necessary, run your pump in the factory location.  Relocating it will cost a lot of money.

### Motor Mounts

These are from RockTactics and are available in both standard and offset for use with the block hugger style headers for about $65.  The bolt pattern is a little odd at 4.410” x 3.078” if you want to make your own.  Chevy ½ ton spring bushings work great.

# Exhaust Manifolds / Headers

The stock exhaust manifolds actually flow pretty good.  Unless packaging is an issue and an aftermarket header, or “block hugger” header is required, I would use them.  Headers are going to add $200-$400 to your engine swap project.  And, the factory collectors are far superior in design and don’t leak compared to the common 3-bolt header flange.  Both are available in steel & ceramic coated.  Summit Headers, & Hooker Headers.  And Earl’s Collector Gaskets are the best I’ve found for the 3 bolt collectors.

O2 Sensors

The factory O2 sensors and “down” pipes are included in the engine turnkey package.  If possible leave them in the factory location.  Otherwise, you will need to locate them somewhere between the exhaust manifold collector and any “Y” pipe, or muffler if you run dual exhaust.  They are Left (bank 1) and Right (bank 2) specific.  Summit Racing sells a variety of O2 weld in bungs.  These work well: SLE-30115  Or, you can cut the factory ones out of the supplied “down” pipes and save yourself a few bucks!

### Oil Pan

The depth (8.75”) of the stock truck oil pan is often an issue.  The most common swap is to the “F” body (camaro / firebird) oil pan at 5.5”.  They can be found on Ebay, LS1Tech, Corvetteforum, and other Forums in the classifieds or from GMPARTSDIRECT.COM for $242. The shallowest pan is the Kevco LS F-Body “gated” pan at 5” deep.  A remote oil filter will be needed with the Kevco pan as well as their specific pickup.  Try to use the factory truck oil pan unless all else fails to save you some money.  Here is a great link to many different oil pans with dimensions & part numbers: LS1Tech-Oil Pans

GM TRUCK PAN		GM F-BODY		   KEVCO F-BODY W/GATES

# Battery

The engine will have the factory positive & negative battery terminals attached to it.  It connects ground to the engine & chassis, and routes the positive led to the starter motor & alternator.  It generally has one other smaller gauge wire that can be used to power the rest of the vehicle.  It is usually located on the front drivers-side of the engine. You can use it, or route your own battery cables.  It is NOT part of the engine run harness.

Water Temp Sensor

There is a factory ECM temp sensor on the drivers side head towards the front.  An additional sensor for an in-cab gauge can be located in the same port of the passenger side head, towards the rear.  Here is the metric to 1/8” NPT adapter: ATM-2277

# ECM Mounting

The ECM (engine control module / computer) is mounted under the hood in the factory truck or suv.  It is completely waterproof and is easiest to mount there.  Although you can locate it in the cab it is not necessary and a large hole in the firewall would be required to pass the connecting plugs through.  M & M Offroad and others make brackets that can be helpful as well.

EGR System Removal / Blockoff (If obtaining your own 1999-2001 Engine)

The EGR system generally needs to be removed unless you need to meet SMOG requirements.  Simple block off plates can be made to cap the exhaust manifolds.  I find it easier / quicker / cheaper to use the parts from the factory system, cut the tubing off and weld the holes closed and bolt back on.  You can use a large rubber cap that will go over the tubing on the port in the manifold or a factory plug is available for about $15 – GM Part number 12558346

# Oil Pressure Sensor & Oil Accumulator

For an aftermarket oil pressure sensor and/or oil accumulator the following ports should be used.  They are primary oil passages, showing oil pressure at the crank, rods, cam, and general “lower end” of the engine.  The factory oil pressure sensor that is located in the rear, behind the intake manifold is a secondary passage and for the ECM.  Although aftermarket billet aluminum blocks can be bought, the factory port block near the oil filter can be easily drilled and tapped to standard NPT threads for access to the primary oil passage.  Otherwise use the forward port shown below with metric to standard adapter.

The port near the

filter is used for an oil

cooler on HD Trucks

and 6.0L vehicles.

For any kind of rock-crawling application I HIGHLY recommend the use of an oil accumulator.  The Moroso or Canton 3 quart versions are the best: MOR-23900

### Radiator

The key to an adequate cooling system is a radiator with a proper fan shroud, and an electric fan will do that (see below).  These engines do not require extra large cooling systems.  The heads are aluminum, the water pump flows well, and they generally dissipate heat easily.  A generic 2-row aluminum radiator in the 24” wide range is usually enough, but if you have additional room, us it.  A dual bypass radiator can add an additional 10% off cooling or so.  A dual bypass with the inlet/outlet on the passenger side is configured well to the GENIII coolant ports.

Cold Air Intake – VERY IMPORTANT

All consideration should be taken to allow the coolest air possible to enter the engine intake.  If there is not a radiator right in front of the intake, an air filter can be attached right to the throttle body.  Otherwise an intake system should be designed to draw air from the side / front of the vehicle.  Behind one of the headlights is a common place.  The hot air from the radiator entering the engines intake will dramatically reduce horsepower in the upper rpm range.  As seen from in the timing table of engine load vs intake air temp, as much as 10 degrees of timing will be removed with an air intake temperature of 190 degrees.  In testing, even well laid out systems often see 120 degrees.  So pay close attention to this in your design.  The cooler the intake charge =  FREE horsepower.

Fan

It has been my experience that the Ford Taurus & Thunderbird electric fans flow more air than any aftermarket fan.  The Taurus 3.8 V6 fan, and V8 Thunderbird fan can be found at Pick-N-Pull anytime for about $35.00.  They are both dual speed and I HIGHLY recommend them.  Depending on your radiator shape, you may want to consider both, as their shape is different.  My wiring harness has provisions from the ECM to control both HI & LOW fan circuits, saving you money as well!  You will have to provide appropriate sized relays.  I have measured the Thunderbird fan on HI to be 25-27amps, and LOW to be around 15amps.  The standard “ice cube” relay will not survive for the high side.  I recommend this 75 amp continuous duty relay from Summit Racing.

Vacuum Port / Break Booster

There is a vacuum port on the back of the intake manifold.  It can be used for a brake booster.  Some engines have a plug here.  The plug can be carefully drilled & tapped to 1/8” NPT to accept a barb fitting for hose hookup.

Gas Pedal & TAC installation

If you have purchased a DBW engine you will have an APP (gas pedal) and TAC module (small black box) with your turnkey engine package.  The gas pedal easily mounts to a vertical surface inside the cab.  The TAC module is weather proof and can be mounted anywhere within reach of the corresponding harness plug and APP wiring.  Avoid high heat locations near exhaust.  Note: The Gas Pedal can be modified if needed.  Shortening the throw will increase throttle sensitivity.  Ensure the sensor maintains full range.  Some came with an adjuster for movable pedals, you will want to remove this portion and attach the actual pedal to the sensor at your desired angle.

PCV Valves & Crankcase Gas Evacuation

The factory crankcase evacuation system draws gases from both valve covers into the intake manifold.  For rock-crawling this can lead to a hydro-locked engine in a roll-over.  Engine oil gets drawn into the intake and further into the cylinders.  I have been happy with evacuating the crankcase gases through the exhaust system.  A venturi is welded into the tail pipe past the muffler and a check valve is threaded on it.  The flowing exhaust gases create a vacuum on the crankcase with little to no possibilities of oil getting into the intake manifold.  It is highly recommended to maintain some sort of POSITIVE crankcase gas evacuation.  Without positive crankcase vacuum, moister and oil sludge builds up decreasing the longevity of the engine.

For HARDCORE rock-crawling, I also recommend relocating the drivers-side valve cover port to the same location as the factory passenger-side valve cover port.  It is easily drilled and tapped to 1/8” NPT and a 90-degree barb fitting threaded in.  Simply cap the factory PCV valve at the rear and leave in place.  This modification will eliminate oil that “puddles” in the rear of the valve cover and subsequently get drawn into the evacuation system on step, near vertical climbs.

COOLANT SYSTEM FILL

I recommend initially filling the coolant system via the water pump outlet port on the top as well as the radiator.  This helps eliminate an air lock, particularly when not using the heater ports.

WIRING HARNESS

Your RTS engine comes with a new engine harness.  Although it has a firewall grommet and the ECM and wire connections can be made inside the cab, it is not necessary.  In factory form the harness and ECM live under the hood.  ALL connections have weatherproof plugs and can handle regular cleaning and average water situations.

Ignition 12V+  (mandatory)

Generally from the crank/run side of keyed source.

Fuel Pump 12V+ (mandatory)

This is the 12V+ from the fuel pump relay.  The relay is controlled by the ECM.  When the ignition is turned on, the fuel pump will cycle approximately 3 seconds and turn off until cranking begins.  Run directly to fuel pump.

Ground 12V- (mandatory)

This is a general ground connection.  Attach to any good ground location on the body or chassis.

------------------------------------------------------------------------------------------------------------------------------------------------------------

STARTER CONNECTIONS

12V+ Main Battery Cable – This is the main cable from your battery.  The engine harness also gets 12V+ power at this connection from the 2 ring terminals also on this connection.

12V- Main Battery Cable – Connect your battery ground cable anywhere that is convenient on the engine.  There are many used bolt holes, or the motor mount bolts work well.

Crank / Start – This connection is provided by you and runs from your key / start button to crank the engine over.  Use a minimum 12ga wire.

------------------------------------------------------------------------------------------------------------------------------------------------------------

MIL (Check Engine Light) 12V- (highly recommended)

This is a ground wire.  Power the MIL (light bulb) with a keyed 12V+, then run this ground wire to the other terminal of the light.

# Speedo, VSS Signal - OUT

This is the signal coming out of the ECM to run a speedometer.  The signal is calculated from the “in” signal & based on tire diameter, & ring/pinion ratios.  Most modern electronic speedometers can read this signal and be easily calibrated.  Only available using the 4L60, 4L80 or aftermarket VSS.

Tach output signal

This is the tach signal from the ECM.  Most tachs can be calibrated to read this signal.  See tach wiring diagram on last page for more info.

FAN 1, Low

This is a GROUND source from the ECM to control engine-cooling fans.  It needs to be routed through an appropriate sized relay.  Connect to negative side of relay coil.  Use the “low” if only one fan will be utilized.  See “FAN” above.  Low, on=202, off=195

#### FAN 2, High

High, on=210, off=203

# Park / Neutral (not a park safety switch)

This is a ground (12V-) that can be utilized when using the 4L60 or 4l80 transmission.  Although not necessary, there are different fuel / air / spark tables for whether you are in gear or P/N.

TCC Brake- (mandatory when using 4L60e or 4L80e Transmission)

TCC Brake Switch Signal is 12V+ when brakes are NOT pressed, and the switch OPENS when you hit the brakes – it is used to unlock the torque converter when brakes are pressed.

TACH WIRING

Sometimes the ECM's tach signal is not strong enough for some aftermarket tach's.  This method can be used to “boost” the signal from the ECM.  All you do is hook one end of a 680 ohm resistor (SUPPLIED BELOW) to the tach wire, and other end of the resistor to a keyed 12V+.  This may not be needed with all tachs and all ECM’s.  The pre 2002 ECM’s and tach combinations seem to be hit-and-miss.  So far, all 2003+ have had to have it.

If you want to use an older factory tach in a retrofit swap let me know.  I can program the ECM for various 4, 6, or 8 cylinder outputs on this signal if your factory tach does not allow you to select 4 cylinders.

Note:  Your tach’s power supply should be a keyed 12V+ source.  So simply use the resistor as a “jumper” between the main 12V+ supply to the tach and the incoming tach signal wire.  Make sure the leads on the resistor aren’t allowed to short to ground as they are unshielded wire and “hot” when the key is on.  Make the connections then cover them and the resister in shrink tubing works well.

Supplied 680ohm, ¼ Watt Resistor

-----------------------------------------------------------------------